--- Half turn Quadrifilar Helix Aerial using wire frame and RG58 coax ---

Frequency 137.50 MHz

Aspect ratio of height to diameter                                1.45

Mean perimeter to wavelength ratio                              1.07

Deviation of perimeter to wavelength ratio              +/- 3.27%

Dimensions                                         Inches                Millimetres

Wavelength                                        85.83909              2180.313

Perimeter                                           88.8444                2256.648

SMALL LOOP:

all measurements are to tube centres

Don't forget these are finished sizes

Diameter                                             14.15742              359.5985

Height                                                 20.52825             521.4178

Length of Helix                                   30.26478             768.7253

Perimeter                                            88.8444               2256.648

LARGE LOOP:

Diameter                                             15.11462               383.9112

Height                                                 21.91619              556.6713

Length of Helix                                   32.31101               820.6996

Perimeter                                             94.85125             2409.222

**************************************************************************